## Slide 1: Restart analysis macro that cycles heating on and off

## Slide 2: Model Diagram
Set natural convection with auto-calculated coefficients as the radiation boundary
Heated Surface (heater)
Heated Body
(1 mm Square Thickness 0.5 mm)
Material: PC
The restart analysis is repeated by automatically switching the boundary condition (heater) of the heating surface to the temperature boundary during heating and to the heat transfer/convection during heat dissipation.

## Slide 3: Analysis Condition (Transient)
The time table setting of the transient analysis is automatically changed to the setting on the Excel worksheet at the time of heating and at the time of heat dissipation.

## Slide 4: Analysis Condition (restart analysis setup)
No import the first time
From the second time onward, restart analysis is automatically performed with reference to the previous result file (PDT).

## Slide 5: Boundary Conditions (Heat Dissipation)
Heat dissipation settings are preset for the model. (Do not change from macro)
In the sample model, the heater (at heat release) and the external boundary condition
Natural Convection (Calculate Coefficients Automatically) is set.

## Slide 6: VBA Macro Interface
Set the green cell, and with the appropriate project file open, click Start Analysis.

## Slide 7: List of macro functions
Function name | Processing Content
FemtetMain | Loop restart analysis while changing analysis and boundary conditions for heating and heat dissipation
AnalysisSetUp | Changing Time Table Settings for heating and heat dissipation Setting Reference PDT for Restart Analysis
BoundarySetUp | Setting the type of boundary condition and temperature corresponding to heating and heat dissipation
SaveResult | Save Results File

## Slide 8: Sample Model Results
After 8 seconds, the temperature rises during heating
and heat dissipation.
The temperature drop coincides with the steady state.